## Slide 2: Autodesk Navisworks Course for Technical Officer (Structural)
Presented by
David Fung

## Slide 3
Introduction to Navisworks File System
 | Autodesk Navisworks Freedom | Autodesk Navisworks Simulate | Autodesk Navisworks Manage
Project viewing |  |  | 
Project Review |  |  | 
Simulation and Analysis |  |  | 
Coordination |  |  | 
Remarks | Open NWD only |  Clash Detection | 

## Slide 4
NWC (Navisworks Cache File)
- interpreter between Navisworks and other software
Navisworks file types
NWF (Navisworks File Set)
- contain links to the original native files (as listed on the Selection Tree) together with Autodesk Navisworks-specific data, such as review markups
- no model geometry is saved
NWD (Navisworks Model)
- contain all model geometry with Autodesk Navisworks-specific data, such as review markups

## Slide 5
Navisworks file types
NWC (Navisworks Cache File)
NWF (Navisworks File Set)
NWD (Navisworks Model)

## Slide 6
Export from Revit to Navisworks (NWC)
https://www.autodesk.co.uk/products/navisworks/autodesk-navisworks-nwc-export-utility

## Slide 7
Export from Revit to Navisworks (NWC)
C:\Program Files\Autodesk\Revit 2018\Samples

## Slide 8
Export from Revit to Navisworks (NWC)

## Slide 9
Export from Revit to Navisworks (NWC)

## Slide 10
Open File

## Slide 11
Background Setting

## Slide 12
Navigate 3D Model

## Slide 13
Dealing with Objects

## Slide 14
Dealing with Objects

## Slide 15
Dealing with Objects

## Slide 16
Selection

## Slide 17
Section View

## Slide 18
Mark-up

## Slide 19
Save NWF

## Slide 20
Combine Models

## Slide 21
Combine Models

## Slide 22
Render Style

## Slide 23
Navigate 3D Model

## Slide 24: Suggested Setting

## Slide 25
Navisworks Settings

## Slide 26
Navisworks Settings

## Slide 27: Quantification

## Slide 28
Setting up workbook

## Slide 29
Dragging items to the workbook

## Slide 30
Taking off the entire model

## Slide 31
Taking off the entire model

## Slide 32
Exporting the takeoff

## Slide 33
Analysis

## Slide 34: Clash Detection

## Slide 35
Clash Detection

## Slide 36
Clash Detection

## Slide 37
Clash Detection
New - a clash found for the first time in the current run of the test
Active - a clash found in a previous run of the test and not resolved
Reviewed - a clash previously found and marked by somebody as reviewed
Approved - a clash previously found and approved by someone
Resolved - a clash found in a previous run of the test and not found in the current run of the test or marked by somebody as resolved

## Slide 38
Clash Detection
Hard:
Detecting actual intersections between geometry
Hard (Conservative) Performing with a conservative intersection method
Clearance Checking for geometry within a specific distance (tolerance) from other geometry
Duplicates Detecting for duplicate geometry

## Slide 39
Clash Detection
Add Test: Adding a new test
Reset All: Resetting all tests. In other words, this will make the clash test status New
Compact All Removing all “Resolved” clash results from the tests to create smaller files
Delete All: Deleting all tests
Run All: Running all tests

## Slide 40
Clash Detection

## Slide 41
Clash Detection
Surface
Line
Points
Self intersect
Current Selection to Clash Selection
Select in Scene (Shown in Selection Tree)

## Slide 42
Clash Detection
Comment
Status
Assigned To

## Slide 43
Clash Detection

## Slide 44
Clash Detection

## Slide 45: Animation_1

## Slide 46
Animation_1

## Slide 47: 4D Construction Sequence

## Slide 48
4D Construction Sequence
3D Model (New Construction/ Existing Building…)
Construction Program/ Master Program
Construction Zoning Plan
Site Layout Plan
Construction Equipment/ vehicle

## Slide 49
Work with TimeLiner

## Slide 50
Work with TimeLiner

## Slide 51
Work with Master Program/ Construction Schedule

## Slide 52
Work with TimeLiner

## Slide 53
Work with TimeLiner

## Slide 54
Work with TimeLiner

## Slide 55
Work with TimeLiner
Planned and Actual show according to the dates.
Planned (Actual Differences) shows things at their planned dates but with color info about real late start or early finish.
Planned against Actual uses the actual dates but includes info if something starts or finishes out of time.
Actual (Planned Differences) shows things at their actual dates but with color info about planned early start or late finish.

## Slide 56
Work with TimeLiner Animation

## Slide 57
Export 4D Construction Sequence (AVI)

## Slide 58: 4D Construction Sequence_Exercise

## Slide 59
TimeLiner_Exercise
Prepare 3D model (NWC)
Prepare Master program by excel (XML => CSV)

## Slide 60
TimeLiner_Exercise

## Slide 61
TimeLiner_Exercise

## Slide 62
TimeLiner_Exercise
Selection Set
Search Set (Find item)
Comments/ User parameters in original source (Revit)
Selection Tree
Quick Properties
Hide/ Unhide
Selection Box
Turn off “Line” rending

## Slide 63
TimeLiner_Exercise

## Slide 64
TimeLiner_Exercise

## Slide 65
TimeLiner_Exercise

## Slide 66
TimeLiner_Exercise

## Slide 67
Animation

## Slide 68
Export 4D Construction Sequence (AVI)
FPS from 8-30
Anti-aliasing between (8x-64x)

## Slide 69: NWD Model Editing_Exercise

## Slide 70
NWD Model Editing_Exercise
Different formats of models received
Open model in Navisworks

## Slide 71
NWD Model Editing_Exercise
Different formats of models received
Open model in Navisworks (Convert to NWD Format)

## Slide 72
NWD Model Editing_Exercise
Check SCALE!!!

## Slide 73
NWD Model Editing_Exercise
Check SCALE!!!

## Slide 74
NWD Model Editing_Exercise

## Slide 75
NWD Model Editing_Exercise
Combine models in Navisworks
3D Model in Navisworks
Construction Equipment/ vehicle in Navisworks
Check Location!!!

## Slide 76
NWD Model Editing_Exercise
Combine models in Navisworks
3D Model in Navisworks
Construction Equipment/ vehicle in Navisworks
Check Location!!!

## Slide 77
NWD Model Editing_Exercise

## Slide 78: Animation_2

## Slide 79
Animation_2

## Slide 80
Animation_2
Capture Object Movement
Capture Object Rotation
Capture Scaling Changes
Capture Color Changes
Capture Transparency Changes

## Slide 81
Animation_2

## Slide 82
Attach with TimeLiner

## Slide 83
Animation_3

## Slide 84
Animation_3

## Slide 85
Animation_3

## Slide 86: Practical

## Slide 87
Exercise

## Slide 88
Appearance Profiler

## Slide 89
Appearance Profiler

## Slide 90
Get Element Location (View Cube)

## Slide 91
Find Elements in Revit

## Slide 92
Switching back to Revit

## Slide 93
Grouping Clash (Manually)

## Slide 94: .----------------------------------
Clipping Planes
To have a better setting on clipping plane:
low number for “Near”
large number for “Far”

## Slide 95: .----------------------------------
Viewpoint Setting
Assign special setting for viewpoint

## Slide 96: Presentation Skill

## Slide 97
Edit Element Object

## Slide 98
Printing
PDF
maximum image size is 2048 x 2048 pixels

## Slide 99
Export Viewpoints Report

## Slide 100: Thank you